## Slide 1: ME469: Advection Stabilization: Achieved through upwind and limiters
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Dissipation and Dispersion Error: Review
Recall, in our modified one-dimensional advection of a passive scalar, we had two types of errors that manifested depending on the underlying numerical approach:
Dissipative-like error:
Dispersion-like error:

## Slide 3: Hybrid-Based Blending
For our general temporal advection/diffusion/source equation, can we define an improved, automatic blended approach between central and upwind?
Recall, the advection operator was:
With (for central, or Galerkin):
And (for first-order upwind):
We can define a blended operator as well:

## Slide 4: Functional form for h – Linked to Peclet number, Pe Many ad-hoc choices, however, a common physical approach is tanh
- peclet_function_form:
velocity: tanh
mixture_fraction: tanh
- peclet_function_tanh_transition:
velocity: 5000.0
mixture_fraction: 2.0
- peclet_function_tanh_width:
velocity: 200.0
mixture_fraction: 4.0

## Slide 5: Hybrid-Blending Sanity Check
Consider a simple fluids case where we have air (298.15K) flowing 1 m/s in a 1 m3 domain
For Pe = 2 at each element, we would require ~0.0305 m resolution, or a mesh of size: ~35,200
Consider a simple fluids case where we have air (298.15K) flowing 10 m/s in a 1 m3 domain
For Pe = 2 at each element, we would require ~0.00305 m resolution, or a mesh of size: ~35,200,000
In general, this constraint results in extremely high mesh counts for most all practical flow configurations that even approach a turbulent flow regime
Moreover, we are blending with upwind – an already shown to be overly diffuse and non-energy conserving

## Slide 6: Monotonic Issues at high Pe: Simple Matrix Analysis
Consider our passive scalar concentration whose natural range (as a mass fraction) is bounded between 0 and unity, here, as a stationary transport equation:
Using our CDS and standard diffusion operator yields the following matrix system:
With coefficients, and:
Substituting: and defining:
Yields:
Positive for Pe < 2
For Pe < 2, the value of the scalar at node i is a linear combination of the neighboring values

## Slide 7: Monotonic Issues at high Pe: Alternative View (Diagonal Dominance)
Define Diagonal Dominance as:
For a monotonic operator and ease of solving the linear system, diagonal dominance is desired
In our advection/diffusion case, this is expressed as:
Which, again, is only ensured when the Peclet number is less than two

## Slide 8: Alternatives to First-order Upwind: Higher-order Upwind – But how on an unstructured mesh?
Recall, that in the finite difference context, we could increase the upwind stencil to increase accuracy, e.g.,
However, for an unstructured setting, this approach is not easily achieved due to the local stencil connectivity
  Recall, we are looping edges (as shown), or elements
Hint… Can we look towards the projected nodal gradient to effectively increase the stencil?

## Slide 9: Classic Flux Limiters Van Leer, B. (1974), "Towards the ultimate conservative difference scheme II. Monotonicity and conservation combined in a second order scheme", J. Comput. Phys., 14 (4): 361–370
Consider our standard three-point stencil obtained by iterating edge 1 and 2
In the above stencil, we are stressing that when iterating edge 2, we do not have information easily obtain for edge 1 (shown above as a dashed line); (speaking from an unstructured perspective)
Above, the “LOW” and ”HIGH” are any operators that you select, e.g.,
i-1
i
i+1
fi+1/2
fi-1/2
ux

## Slide 10: Flux Limiter Definition
Sweby (1984) defined set of permissible limiter regions for the desired second-order accurate methods: A sampling of the Sweby Diagram
For a monotonically increasing function, TV(f) = |f1 −fN |. Note that if f1 and fN are taken constant, then, as long as the function remains monotonic the total variation is constant
However, if TV(f) increases, then this suggest oscillations in the solution have occurred
Sweby's 2nd order TVD region. Created in Matlab. Griffgruff 18:37, 11 October 2006 (UTC)
Superbee:
Van Leer:
Symmetry property:
Total Variation:

## Slide 11: General Kappa-Method of Hirsh Numerical Computation of Internal and External Flows, vol. 2, John Wiley & Sons, 1990
For the edge defined by the i and i+1 node, define a Left and Right state:
For k = +1, we simply revert to CDS
For k = -1, Second-order upwind
For k = 2/3, QUICK (Leonard, “A stable and accurate convective modelling procedure based on quadratic up-stream interpolation”, Comput. Methods Appl. Mech. Eng. 19 (1979) 59–98.)
Assignment: Algebra!!!

## Slide 12: Kappa = 0 Method of Hirsh Numerical Computation of Internal and External Flows, vol. 2, John Wiley & Sons, 1990.
For k = 0, recast as:
Where,
Above, define a “limiter” function that “senses” when the solution is smooth (tends towards unity) and when the solution is oscillatory (tends towards zero)
Assignment: Algebra!!!
Derived by substituting k = 0, and
using the projected nodal gradient
definition – or – just by noting an
extrapolation using a gradient

## Slide 13: Blending Approaches to Arrive at Pseudo Higher-order Methods: Upwind and Central
Define an upwind operator now at an arbitrary integration point:
And for a generalized CDS scheme:

## Slide 14: The Idealized Stencil Set
With Nalu input file specifications
- alpha_upw:
velocity: 1.0
- alpha:
velocity: 1.0
- upw_factor:
velocity: 1.0
- limiter:
velocity: yes
(zero reverts
to first-order)

## Slide 15: Pseudo 4th order Verification Results
Verification using Central (linear and quadratic) compared to pseudo 4th order
Lower error, however, still formally second-order accurate