## Slide 1: ME469: Common Discretization Approaches
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Lecture Objectives
The Concept of Meshing
Why Unstructured?
Unstructured Element Types
Cell-centered Finite Volume (FV)
Edge-based Vertex-Centered (EBVC)
Control-Volume Finite Element Method (CVFEM)
Finite Element Method (FEM)
Staggered arrangement

## Slide 3: Introducing a Mesh over Heart Domain, W
Geometry is:
Complex
Curved
Sharp

## Slide 4: Re-introducing a [Finite Difference] Mesh over Heart Domain, W
Geometry is:
Complex
Curved
Sharp

## Slide 5: Re-introducing a [Finite Difference] Mesh over Heart Domain, W
Not impossible: Chertock, et al., “A Second-Order Finite-Difference Method for Compressible Fluids in Domains with Moving Boundaries”, Commun. Comput. Phys., 2018
Geometry is:
Complex
Curved
Sharp

## Slide 6: Introducing a [Structured Mesh] over Heart Domain, W;
Geometry is:
Complex
Curved
Sharp

## Slide 7: Introducing a [Structured Mesh] over Heart Domain, W;
Geometry is:
Complex
Curved
Sharp

## Slide 8: Introducing a [Structured Mesh] over Heart Domain, W;
Geometry is:
Complex
Curved
Sharp

## Slide 9: Structured vs Unstructured
Many times, canonical flows of interest are represented by simplified geometries that allow for cartesian meshes – with “stair-stepping”
Ret 395 plane-channel (Jofre, Domino, Iaccarino, 2018)
https://www.itascainternational.com/software/introduction-to-meshing
Often times, not!
RANS-based backward facing step (Domino, 2012)

## Slide 10: Example: The Carbon-Capture Multidisciplinary Simulation Center
http://ccmsc.utah.edu/about.html
15MW coal-fired boiler volume rendered image of large (90 mm) particles
Staggered schemes have been demonstrated to support complex applications
Cut-cells and embedded approaches help

## Slide 11: Attributes of an Element
An element consists of nodes, edges, and faces
face
edge
centroid
node (or vertex)
Hex8, i.e., eight-node hexahedron
8 nodes
6 faces
12 edges

## Slide 12: Examples of Various Topologies
Hex8
Tet4
Pyramid5
Wedge6
Arbitrary
Higher-order promoted elements (Hex27, Tet10, Wedge16, Hex64, etc.)

## Slide 13: Introducing a Mesh over Heart Domain, W
Elements of size 4 (Quad4) or 3 (Tri3) have been introduced
Exterior domain is faceted
Non-conformal interface between the Tri3 and Quad4 block
Two types of connectivity have been presented: node:element and element:face:element
Two types of integration: We vs Wcv

## Slide 14: Data Structure Ramifications: A bit more complex…
Element and associated data structures are indexed directly via ith and jth location, e.g., temperature (i,j), over the range: temperature(0:nX-1,0:nY-1)
Neighbors are directly indexed, e.g,, “north” neighbor of (i,j) is (i,j+1)
Element and associated data structures are indexed indirectly via a data structure, e.g., temperature(k), over the range: temperature(0:nElem-1)
Nodes of element(k) are obtained via connectivity relationship mappings
  std::vector<mesh_type> nodes = elem_nodes (k)
Nodal fields, for element k via:
  pressure = field_data(nodes[0,..,numElem)
temperature(i,j)

## Slide 15: Integration Over the Domain: The ”Finite” in Finite-Volume and Finite Element
Consider a simple model equation with the heart domain in mind:
Integrating over the entire domain, W:
Without loss of generality, let us define a set of subdomains, Wk:
As present, only volumetric integrals appear
Note: The formality of Sk and Wk is implied to exist over the full domain and is often times dropped – integral type implied by dV and dS
Where Fj is a flux and S is a source term

## Slide 16: Fundamentals of Discretization: Surface vs Volume Integrations
Given a partial differential equation (PDE) and associated volumetric form:
Applying Gauss Divergence provides the standard finite volume form for fluxes in surface integral form:
We can also multiple PDE by an arbitrary test function, w, and integrate over a volume,
Next, integrate by parts and apply
Gauss-Divergence. Note, that test function must be differentiable – shown here, at least once..

## Slide 17: Define a Stencil: Element:Face:Element
Cell-centered, finite volume (shaded region)
  Degree of freedom (DOF), i.e., solution, resides at the centroid of the element

## Slide 18: Define a Stencil: Element:Face:Element
Cell-centered, finite volume (shaded region)
  Degree of freedom (DOF), i.e., solution, resides at the centroid of the element
face
(in 2D, also an edge)
centroid
(DOF)
element

## Slide 19: Define a Stencil: Element:Face:Element
Cell-centered, finite volume (shaded region)
  Degree of freedom (DOF), i.e., solution, resides at the centroid of the element
Connected
DOFs

## Slide 20: Define a Stencil: Element:Face:Element
Cell-centered, finite volume (shaded region)
  Degree of freedom (DOF), i.e., solution, resides at the centroid of the element
Surface integration
points

## Slide 21: Define a Stencil: Element:Face:Element
Cell-centered, finite volume (shaded region)
  Degree of freedom (DOF), i.e., solution, resides at the centroid of the element
Volume integration
point

## Slide 22: Define a Stencil: Node:Edge:Node
Edge-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex

## Slide 23: Define a Stencil: Node:Edge:Node
Edge-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex
node
(vertex of an element)
edge
(of an element

## Slide 24: Define a Stencil: Node:Edge:Node
Edge-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex
Connected
DOFs

## Slide 25: Define a Stencil: Node:Edge:Node
Edge-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex
Surface integration
points

## Slide 26: Define a Stencil: Node:Edge:Node
Edge-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex
Volume integration
point

## Slide 27: Define a Stencil: Node:Element:Node
Choice #1, Element-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex

## Slide 28: Define a Stencil: Node:Element:Node
Choice #1, Element-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex
Surface integration
points

## Slide 29: Define a Stencil: Node:Element:Node
Choice #1, Element-based, vertex (or node)-centered finite volume (shaded region)
  Degree of freedom, i.e., solution, resides at the node, or vertex
Volume integration
points

## Slide 30: Define a Stencil: Node:Element:Node
Choice #2, Element-based, finite element
  Degree of freedom, i.e., solution, resides at the node, or vertex

## Slide 31: Define a Stencil: Node:Element:Node
Choice #2, Element-based, finite element
  Degree of freedom, i.e., solution, resides at the node, or vertex
Volume integration
points

## Slide 32: VOF Transport Discretization Nuance: Volume- or Surface-based?
Simple enough, define the volume (fraction) of fluid (absent evaporation):
Option 1: volumetric-form:
Option 2: divergence-form:
CVFEM/FEM (really, any element-based approach)
Evaluated as a volumetric-contribution (diamonds)
Traditional finite volume (element, edge, cell-centered)
Evaluated as a surface integral (triangle)
Allows for a consistent advecting velocity (mass conserving)
that is obtained from the continuity equation
Gauss-Divergence

## Slide 33: Reality: Meshing time for complex applications remains a significant bottleneck!
Many applications of interest contain complex geometries low-Mach fluids users interested in high-quality simulation results tend towards hexahedral-based topologies (if possible)
However, if a scheme is “design-order” accurate, any topology may suffice as it is simply a matter of mesh size and efficiency – not unlike the active discussion on low- vs higher-order
Sometimes, the penetration of a low-Mach fluids physics addition in common analysis is high as the meshing can be prohibitively complex
Example: Vestas V27 225 kw hybrid low-order Hex8/Tet4/Pyr5/Wedge6
Very complex world – stair-stepped!

## Slide 34: Classic Staggered Finite Volume
Velocity degree-of-freedom is staggered relative to pressure and other primitives, e.g., enthalpy, mixture fraction, etc.
Stencil for CC-quantities
Stencil for x-velocity
Stencil for y-velocity
PN
PS

## Slide 35: Attributes of a Staggered Scheme
By design, non-orthogonality is absent, however, complex geometry will be stair-stepped
From a fluids perspective, the operators are ideal, i.e., pressure gradient for momentum is compact, e.g., (PE – PW)Dx-1
As will be seen in future lecture topics, the skew-adjoint nature of the Divergence operator, D, and Gradient operator, G, allows for a Laplace operator, L = DG
Can be extended to higher-order
Frequently, meshing complex geometries can be extremely difficult (consider our V27 example)

## Slide 36: An Informal Survey….
Cell-Centered: (Sometimes generalized Polyhedra)
  Ansys Fluent, OpenFOAM (FireFOAM, NavyFOAM), CD-Adapco (Star-CCM), Soleil-X (Stanford)
EBVC: (Most typical in the acoustically compressible space)
  SU2, FUN3D, CHAD, Nalu-Wind (production), Nalu (option to explore discretizations)
CVFEM
  Fluent (originally!), CFX-TASC-FLOW, Sierra Fuego (SNL), Nalu
FEM
  FIDAP, COMSOL, EDDY (NASA), AcuSim, PHASTA
Staggered
  Arches (Utah)

## Slide 37: An Informal Survey….
Cell-Centered: (Sometimes generalized Polyhedra)
  Ansys Fluent, OpenFOAM (FireFOAM, NavyFOAM), CD-Adapco (Star-CCM), Soleil-X (Stanford)
EBVC: (Most typical in the acoustically compressible space)
  SU2, FUN3D, CHAD, Nalu-Wind (production), Nalu (option to explore discretizations)
CVFEM
  Fluent (originally!), CFX-TASC-FLOW, Sierra Fuego (SNL), Nalu
FEM
  FIDAP, COMSOL, EDDY (NASA), AcuSim, PHASTA
Staggered
  Arches (Utah)
Common Water-Cooler CFD Arguments:
Structured vs. Un-structured
FEM vs. Finite Volume
Node-centered vs. Cell-centered
Monolithic vs. Operator Split
Compressible vs. (acoustically) Incompressible
Explicit vs. Implicit

## Slide 38: An Informal Survey….
Cell-Centered: (Sometimes generalized Polyhedra)
  Ansys Fluent, OpenFOAM (FireFOAM, NavyFOAM), CD-Adapco (Star-CCM), Soleil-X (Stanford)
EBVC: (Most typical in the acoustically compressible space)
  SU2, FUN3D, CHAD, Nalu-Wind (production), Nalu (option to explore discretizations)
CVFEM
  Fluent (originally!), CFX-TASC-FLOW, Sierra Fuego (SNL), Nalu
FEM
  FIDAP, COMSOL, EDDY (NASA), AcuSim, PHASTA
Staggered
  Arches (Utah)
Common Water-Cooler CFD Arguments:
Structured vs. Un-structured
FEM vs. Finite Volume
Node-centered vs. Cell-centered
Monolithic vs. Operator Split
Compressible vs. (acoustically) Incompressible
Explicit vs. Implicit

## Slide 39: Hybrid Meshes, Even for LES!
Hybrid mesh study based on Ham and Iaccarino, CTR Annual Brief, 2006, found that simulations were extremely sensitive to mesh topology
Non-symmetric time mean flow found for cell-centered; better for the CTR node-centered formulation
Native CVFEM and EBVC are both symmetric in mean quantities
Domino, et. al, “The suitability of hybrid meshes for low-Mach large-eddy simulation” Stanford CTR Summer Program, 2018

## Slide 40: Recent Generalized Unstructured Findings
Domino, et. al, “An assessment of atypical mesh topologies for low-Mach large-eddy simulation”, Comput. Fluids (2019)