## Slide 1: ME469: Common Discretization Approaches: Edge-based,Vertex-Centered (EBVC), and Cell-Centered (CC)
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Review of Discretization Options
Degree-of-freedom (DOF) for:
  Cell-centered: Stencil is based on an element:face:element
  DOFs at vertices of elements, or “nodes”, element:node (CVFEM, FEM), edge:node (EBVC)

## Slide 3: Review of Discretization Options: New, a nodal-basis…
Definition of an interpolation function:
is the Lagrange function associated with node n
is the value of the DOF at node n
The nodal basis functions obey equipartition of unity and satisfy,
Degree-of-freedom (DOF) for:
  Cell-centered: Stencil is based on an element:face:element
  DOFs at vertices of elements, or “nodes”, element:node (CVFEM, FEM), edge:node (EBVC)

## Slide 4: Three Finite Volume Stencils

## Slide 5: Fundamentals of Discretization: Surface vs Volume Integrations
Given a partial differential equation (PDE) and associated volumetric form:
Applying Gauss Divergence provides the standard finite volume form for fluxes in surface integral form (no distinction between internal control volume faces and boundary faces):
We can also multiple PDE by an arbitrary test function, w, and integrate over a volume,
Next, integrate by parts and apply
Gauss-Divergence. Note, that test function must be differentiable – shown here, at least once..
Interior
Boundary

## Slide 6: In Contrast: Finite Difference (For Our Simple Model Equation)
With terms: time, advection and diffusion
For a finite difference, centered (2nd order stencil), the continuous PDE can be discretized as:
Noting, above the n+1 fully implicit approach that is solved over the finite difference “mesh”
What is an alternative? Finite-volume/element…..
Central finite difference
Forward finite difference
Backward finite difference
j
J+1
J-1
J-2
J+2

## Slide 7: Cell-Centered (CC) and Edge-Based Vertex-Centered (EBVC): Each are generally a two-state scheme, Left (L) and Right(R)
CC (A) and EBVC (B) – As shown below, each have a set of common features
  Class Discussion: What are the common features?
(A)
(B)

## Slide 8: Cell-Centered (CC) and Edge-Based Vertex-Centered (EBVC): Each are generally a two-state scheme, Left (L) and Right(R)
CC (A) and EBVC (B) – As shown below, each have a set of common features
  Class Discussion: What are the common features?
(A)
(B)
Volume integration
point (single)

## Slide 9: Cell-Centered (CC) and Edge-Based Vertex-Centered (EBVC): Each are generally a two-state scheme, Left (L) and Right(R)
CC (A) and EBVC (B) – As shown below, each have a set of common features
  Class Discussion: What are the common features?
(A)
(B)
Surface integration
point (single)

## Slide 10: Cell-Centered (CC) and Edge-Based Vertex-Centered (EBVC): Each are generally a two-state scheme, Left (L) and Right(R)
CC (A) and EBVC (B) – As shown below, each have a set of common features
  Class Discussion: What are the common features?
(A)
(B)
Surface integration
point (single)
Virtual edge
Connected by a left and right DOF-
Each at the control volume face

## Slide 11: The Control Volume for CC is Defined by the Element Volume
All primitives are collocated at the cell-center of the element with equal-order interpolation
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
Iterate Elements for volume-based contributions
Iterate Virtual-Edges or Control Volume Faces for surface-based contributions
TL
TR
nj

## Slide 12: The Control Volume for EBVC is Defined by the Dual-Volume
All primitives are collocated at the vertices of the elements with equal-order interpolation
A dual mesh is constructed to obtain flux and volume quadrature locations
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
Iterate Nodes for volume-based contributions
Iterate Edges for surface-based contributions
Dual-volume definition
Edge-based stencil
Area vector
Dual nodal volume
nj
TL
TR

## Slide 13: One-Dimensional Example of a Non-Uniform Mesh
The nodes of the mesh need-not be equally spaced
node = 0
1
2
3

## Slide 14: Control Volumes for CC and EBVC
Note: Switched depiction of node (or vertex) to the cell-centered location
node = 0
1
2
3
x
x
x
2
3
x
x
x
x
CC = 1

## Slide 15: Control Volumes for CC and EBVC
Note: Switched depiction of node (or vertex) to the cell-centered location
node = 0
1
2
3
x
x
x
x
x
x
x
2
3
CC = 1

## Slide 16: Control Volumes for CC and EBVC
Face-centered vs Cell-Centered
node = 0
1
2
3
x
x
x
x
x
x
x
Cell-centered
Face-centered
2
3
CC = 1

## Slide 17: Basis Function Re-Visited
Define an iso-parametric base element that varies from -1:+1, with integration point at the location x: - defining Lagrange interpolation function,
node = 0
1
2
3
x
x
x
x
x
x
x
Face-centered
Cell-centered
2
3
CC = 1

## Slide 18: Basis Function Re-Visited
node = 0
1
2
3
x
x
x
x
x
x
x
Face-centered
x
1 2
x = 0
Cell-centered
23
2
3
CC = 1
Define an iso-parametric base element that varies from -1:+1, with integration point at the location x: - defining Lagrange interpolation function,

## Slide 19: Basis Function Re-Visited
node = 0
1
2
3
x
x
x
x
x
x
x
Face-centered
x
x
1 2
1 2
x = 0
x = 1/2
Cell-centered
23
23
2
3
CC = 1
Define an iso-parametric base element that varies from -1:+1, with integration point at the location x: - defining Lagrange interpolation function,

## Slide 20: Other Examples of a Basis (This will become important for the element-based schemes)
Two-dimensional promotion
Quadratic (Bar3)
1 3 2
Linear (Quad4)

## Slide 21: Model Passive Scalar Transport: Introducing the Test Function, w
Time/Src/Advection/Diffusion equation for scalar f
Under the assumption, yields:
We can also integrate this PDE over the volume, while introducing a test function, w
The above is the so-called weak-form of the original (strong form) partial differential equation
The elegant concept of a weighted residual statement is to seek a weak solution such that the residual is orthogonal to a selected space of weight functions

## Slide 22: Model Passive Scalar Transport: Integration-by-Parts
Recall, integration-by-parts, for example,
Note, that w must be differentiable at least once
Under the special designation of w to be a piecewise constant, or Heaviside function, the gradient of this is a (negative) Dirac delta function
A key property of this function is that the gradient of the piece-wise constant test function is a distribution of delta functions on the sub-control volume surface yielding,
Recall, we could have arrived at this form by simply usage of Gauss-Divergence, however, this formality allows us to view a finite volume scheme as a Petrov-Galerkin scheme, i.e., the underlying basis differs from the test function

## Slide 23: Deep Dive on EBVC: Node and Edge-loops
EBVC is a discretization scheme that:
Uses a piecewise-constant test function
Is a two-state flux approach, with a face-centered arrangement
Iterates over locally-owned nodes for Time/Source/etc. (volumetric-based terms)
Iterates over locally-owned edges for Advection/Diffusion terms (surface-based terms)
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n2
n1 (L)
n2 (R)
e1
Notes For Assembly Procedures:
Surface normal points from L to R nodes
Contributions added to the L, subtracted from the R

## Slide 24: EBVC: Implicit Time Discretization
Let us define a general implicit time integrator that is A-stable
  For y’ = k y ; y(0) = 1; y(t) = ekt solution approaches zero as time increases for k < 0
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over a nodal iteration and uses a single integration point (known as mass-lumping)
For uniform time stepping, the coefficients are given by, g1 = 3/2 g2 = -2 g3 = 1/2
n2

## Slide 25: EBVC: Implicit Time Discretization; Code
https://github.com/NaluCFD/Nalu/blob/master/src/ScalarMassBDF2NodeSuppAlg.C

## Slide 26: EBVC: Source Term Discretization
Source terms for the edge-based scheme are also assembled over a nodal loop
Note that in this scheme, we are using single point quadrature, i.e., the function is evaluated at a single point
The single point integration point leverages the fac that: p = 2N -1
Where N is the number of integration points and p is the polynomial order
For a linear basis, using one-point quadrature is design-order, or second-order in space
n2

## Slide 27: EBVC: Source Term Discretization; Code
https://github.com/NaluCFD/Nalu/blob/master/src/user_functions/VariableDensityMixFracSrcNodeSuppAlg.C

## Slide 28: EBVC: Advection Term Discretization
For advection, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
Recall, that the mass flow rate at an integration point is prescribed
Moreover, since the integration point is at the edge mid-point, fip = (fR + fL)/2
This is a central- or Galerkin-based advection operator; shown in conservative form, i.e, is in divergence form and has been integrated-by-parts
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1

## Slide 29: EBVC: Advection Term Discretization
For advection, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
Recall, that the mass flow rate at an integration point is prescribed
Moreover, since the integration point is at the edge mid-point, fip = (fR + fL)/2
This is a central- or Galerkin-based advection operator; shown in conservative form, i.e, is in divergence form and has been integrated-by-parts
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1
For kinetic energy
conservation, a CC
scheme also
uses ½ weights!
Mahesh et al., JCP (2004)

## Slide 30: EBVC: Advection Term Discretization: Central
For advection:
j-1
j
j+1
j+1/2
j-1/2
State n or n+1

## Slide 31: EBVC: Advection Term Discretization; Code
https://github.com/NaluCFD/Nalu/blob/master/src/AssembleScalarEdgeSolverAlgorithm.C

## Slide 32: Upwind Advection Operators
Recall from our finite difference class that in absence of a stabilizing diffusion term, or when the velocity is very high, i.e., the Peclet number > 2, non-physical oscillations can be noted
An upwind approach was devised to mitigate this at the expense of numerical accuracy
For a finite volume approach, upwinding is very easy to construct
However, upwind operators, even if higher-order, are numerically dissipative due to loss of symmetry of the operator
Higher-order upwind (second-order in space) can be obtained on an unstructured mesh by use of projected nodal gradients and extrapolation (will cover this in the advection operator section)
“as the wind blows”
j-1
j
j+1
fj+1/2
fj-1/2

## Slide 33: EBVC: Diffusion
For diffusion, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1

## Slide 34: EBVC: Diffusion, Non-Orthogonality
The edge-based diffusion operator is a bit more complex in that we are computing a gradient at the integration point while using two nodes, the left and right
In many practical meshes, the distance vector between the edges (dxj) and the edge area vector will not be perfectly orthogonal
This non-orthogonality causes inaccuracy when using a simplified approach
The non-orthogonality approach of Jasek (Ph.D. Imperial College) is a standard cell-centered approach that has been adopted for edge-based schemes
CC and EBVC are each two-state schemes and share non-orthogonality issues
n2 (L)
n3 (R)
e2
Where Gjf is a “projected nodal gradient”
and,

## Slide 35: EBVC: Diffusion, Non-Orthogonality
The edge-based operator:
j-1
j
j+1
j+1/2
j-1/2
State n or n+1

## Slide 36: (Projected) Nodal Gradient Operator
Recall, that the edge-based diffusion operator, and as we will see in future lectures for some choices for the advection operator, a nodal gradient is required
First, the gradient of a function (other than linear) is discontinuous, i.e., the value at a shared element face depends on which element is used to compute the gradient
Therefore, we can view the nodal gradient a continuous at the nodes and discontinuous within the elements
Let’s minimize this difference:
by solving:

## Slide 37: EBVC: Diffusion, Non-Orthogonality; Code
https://github.com/NaluCFD/Nalu/blob/master/src/AssembleScalarEdgeDiffSolverAlgorithm.C

## Slide 38: Typical Difficulties for a Two-State Scheme
With two points, only a linear basis can be used, therefore, unstructured CC and EBVC are limited to second-order spatial accuracy
Non-orthogonality, or the mis-alignment of the distance vector between the two ”L” and “R” states and the surface normal, is present
Both edge- and cell centered-based schemes show degraded accuracy of the diffusion operator on generalized unstructured meshes
Several non-orthogonality approaches are available, for the best source, see Jasak
  Jasak, “Error analysis and error estimation for the finite volume method with applications to fluid flow”, Imperial College Dissertation, 1996
  Projected nodal gradient:
    Expands stencil
    Is generally used in a deferred correction context, i.e., any matrix contribution is lagged and only appears in the residual
nj
Dxj
nj
TL
TR

## Slide 39: For Instance, Verification of The Diffusion Operator

## Slide 40: Arbitrary Polyhedra
Thus far, we have described the element types as rather simple, e.g., Hex, Tet, Pyramid, and Wedge (or Prism)
What if the element type was arbitrary and designed to minimize non-orthogonality?
  Bres et al., “Large-eddy simulations of co-annular turbulent jet using a Voronoi-based mesh generation framework”, 2018 AIAA/CEAS Aeroacoustics Conference
  Two-state limited to second-order-in-space (extensions exist)
Ansys-based arbitrary polyhedra
Exercised by https://cfd.ninja

## Slide 41: Simple One-D Diffusion Example
Let us introduce (briefly) the Method of Manufactured Solutions (MMS)
Consider a simple diffusion equation:
with a presumed, or manufactured solution:
Gauss-Divergence
Discrete flux-based form at the sub-control volume surface (scs) and sub-control volume IP:
With error:

## Slide 42: Simple One-D MMS Example; Edge-based Assemble of Diffusion
We will use a linear basis and solve this system over a small patch of linear bar elements
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
Dx = 1
x
x
x
node = 0
1
2
3
Edge 1

## Slide 43: Simple One-D MMS Example; Edge-based Assemble of Diffusion
We will use a linear basis and solve this system over a small patch of linear bar elements
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
Dx = 1
x
x
x
node = 0
1
2
3
Edge 2

## Slide 44: Simple One-D MMS Example; Edge-based Assemble of Diffusion
We will use a linear basis and solve this system over a small patch of linear bar elements
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
Dx = 1
x
x
x
node = 0
1
2
3
Edge 3

## Slide 45: Simple One-D MMS Example; Collect all of the terms
Correct for BCs
Fully assembled
system
Fully assembled
matrix
Solution is exact….. Linear basis exactly captures a quadratic solution

## Slide 46: Compare/Contrast to previous FD
FV:
Divide by Volume, V, and density (constant velocity)
Matches FD!
j-1
j
j+1
j+1/2
j-1/2
State n or n+1
State n or n+1

## Slide 47: EBVC and CC Review
Each are two-state (left and right schemes)
Nominally, second-order in space due to limited stencil and connectivity
Fast, efficient
Diffusion operator may suffer on non-orthogonal meshes
CC is common in many commercial and open-source codes, e.g., Ansys Fluent, OpenFOAM
Edge-based more often seen in compressible codes
Exercise: Derive upwind operator for EBVC…..
For more information, see: B. Diskin, J.L. Thomas, “Comparison of node-centered and cell-centered unstructured finite-volume discretizations: inviscid fluxes”, AIAA J. 49 (4) (2011) 836–854.
“as the wind blows”
j-1
j
j+1
fj+1/2
fj-1/2

## Slide 48: Linking to 1d_quad4_adv_diff
Recall, the transport equation for the 1d_quad4_adv_diff laboratory exercise is as follows:
where
For now, let’s focus on the advection term. We know that we can integrate over the volume and simply compute this term at the volume integration points,
Option: scv_advection_np
As with the volume of fluid equation on the previous slide, we can also write this term as:
that can be simplified (for constant velocity)
Option: scs_advection_np (or scs_upw_advection_np)