## Slide 1: ME469: High Performance Computing for CFD
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: High Performance Computing for CFD: Outline
Overview of Time and Length Scales
  Fire
  Wind
Conceptual Parallel Computing Model
Types of Scaling: Strong and Weak
Examples of Scaling
Next Generation Platform Exascale Drivers
Data Movement vs Data Execution
Conclusions

## Slide 3: Disparity in Time and Length Scales, Fire
Engineering Scale of Interest
Convective Transport
Heat Transfer in Weapon
Flames
Chemical Kinetics
Molecular Transport
Diffusive Transport
Soot
Products
Fuel Distribution
Convection
Molecular Radiation
Soot Radiation
Soot Growth
10-10
102
10-8
10-6
10-4
10-2
100
Length Scale, meters
Time Scale, seconds
10-12
10-9
10-6
10-3
100
103

## Slide 4: Disparity in Time and Length Scales, Wind
Engineering Scale of Interest
Convective Transport
104
10-6
10-4
10-2
100
102
Length Scale, meters
Time Scale, seconds
10-6
10-3
100
103
Knight & Carver
Severe Leading Edge Erosion
Sound propagation (turbulent atmosphere and complex domains)

## Slide 5: Routine Examples of HPC
O(6) billion wind energy application
O(2) billion DNS impinging jet, velocity (vertical) and heat flux; Q-criterion
O(200) million multi-physics fire

## Slide 6: Conceptual Scaling Exercise
Goal: Paint a house in one day
  My House: 1000 sq ft
WH: 60,000 sq ft
One person would paint my house in two days (!!)
The white house will require one person 120 days (!!)
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend

## Slide 7: Single House, More People (each person with reduced load)
Goal: Paint a house in one day
  My House: 1000 sq ft
WH: 60,000 sq ft
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend
+
= One day
+
= Faster Completion; Half day (each person 250 sq ft)
+
+

## Slide 8: White House, More People (with shared load)
Goal: Paint a house in one day
  My House: 1000 sq ft
WH: 60,000 sq ft
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend
( )
= 60 days
= 1 day
60x
Time to completion is one day. Everyone
involved provided 500 sq ft
+
+

## Slide 9: Single House, More People (with impediments)
Sam’s team, who played basketball last night, have some injuries
Limited paint brushes…
Plenty of paint, poor loading capacity
No coherent plan of attack
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend
…
= 60 days
+
+
~ 250 sq ft/day
+
( )
60x
n
>> 1 day

## Slide 10: Types of Scaling
Strong Scaling: How the solution time varies with increased computational resources (cores, threads, GPU/Warps) on a fixed-size problem
User Y has a mesh that is 1 billion elements and would like to minimize the time it takes to complete a simulation; the larger the resource, the faster the turn-around
Weak Scaling: How the solution time varies with increased problem size on a fixed computational resource load (cores, threads, GPU/Warps)
User Y is conducting a validation study that includes three mesh resolutions, which were obtained by uniform mesh refinement, and would like to increase the computational resource appropriately for each subsequently refined mesh

## Slide 11: Types of Scaling
Strong Scaling: How the solution time varies with increased computational resources (cores, threads, GPU/Warps) on a fixed-size problem
User Y has a mesh that is 1 billion elements and would like to minimize the time it takes to complete a simulation; the larger the resource, the faster the turn-around
Weak Scaling: How the solution time varies with increased problem size on a fixed computational resource load (cores, threads, GPU/Warps)
User Y is conducting a validation study that includes three mesh resolutions, which were obtained by uniform mesh refinement, and would like to increase the computational resource appropriately for each subsequently refined mesh
~4,000 elem/core
~8,000 elem/core
General Implicit Guidelines:
1e6 elem/node
~25k elem/core

## Slide 12: Challenges Associated with Scaling
Consider a communication-intensive code procedure: Algebraic Multigrid (AMG) preconditioner setup
  Hierarchy of parallel
Point-to-point communications
Like verification, the product of a first-time scaling study at a new production scale is generally met with work!

## Slide 13: Computing Performance: Through the Years
HPC is facing a new disruption in technology
Mainframes
60’s to 70’s
Vector
Supercomputers
70’s to early 90’s
Technology disruptions require a significant increase in complexity of our codes
MPP w/ Advanced Architecture nodes: Multilevel, heterogeneous, energy and memory constrained
ROOM  MACHINE  CABINET  CHIP
COMPLEXITY
Massively parallel processor (MPP) systems with simple nodes
1990’s to 2010
HPC is facing a new disruption in technology
Slides courtesy of Mike Glass, Jim Ang, Rob Hoekstra, Si Hammond, Ron Brightwell, and Stephen Olivier.

## Slide 14: Drive Towards Next Generation Platforms
Chart: Memory / Core
| Purple ('05) | Red Storm ('05) | Dawn ('09) | Cielo ('10) | TLCC2 ('11) | Sequoia ('12) | Future (est.)
Mem/core | 4 | 2 | 1 | 2 | 2 | 1 | 0.2
B:F | 1.6 | 0.44 | 1 | 0.86 | 0.83 | 0.22 | 0.03
Dramatic increase in on-node parallelism and reduction in relative data movement is counter to our current code performance
Power constraints are driving the rapid increase in on-node parallelism.
However, per core memory bandwidth is decreasing making it extremely difficult to fully utilize additional cores
Slides courtesy of Mike Glass, Jim Ang, Rob Hoekstra, Si Hammond, Ron Brightwell, and Stephen Olivier.

## Slide 15: High Performance Computing (HPC): Enabling Scientific Advancement
  Late Roman Timeline 250 AD - 300 AD
250 AD: The Goths invade Anatolia (AKA, Asia Minor), in sea-borne raids they plunder Nikopolis
Trinity open-science Domino and Barone, SAND2016-4085C (2016) to elucidate stall cells
O(6) billion element wind energy application (high-Re flow past thick blade in high AoA
O(128,0000) core run for ~one week ~1800 year simulation using computing resources available 10-years ago: Complete in roughly 29 years!
Recent impinging jet study: 200,000,000 CPU hours (~23,000 years)
25C, 100C, 300C, and 600C case run on 2000-4000 nodes (32 and 64 mpi ranks/node)
GPU-based approaches now emerging
A giant at redwood tree illustrating the passage
of time within its’ growth rings
Lin et al., Parallel Proc. Letters, (2014)

## Slide 16: Parallel Strategies: Option 1
Sierra Toolkit/Standard Ownership rules: Mesh object (nodes, edges, faces, elements) owned by lower-rank. For example:
P0 locally owns E1 and nodes 1, 2, 4, and 5
P1 locally owns E2, E3, and E4 and nodes 3, 6, 7, 8, and 9
P0 and P1 share nodes 2, 4, and 5
Desired Control-Volume Finite Element (CVFEM) Operation:
“nodal volume” assemble for node 5 via iteration of each 1cmx1cm element. Desired nodal volume for node 5 = 1 cm2 exactly the same on both parallel ranks
Options:
1. Iterate over locally owned elements and locally accumulate nodal volume field followed by a parallel sum and copy owned to shared.
2. Ghost element E2, E3, and E4 to P0 and E1 to P1 (along with coordinates) and iterate locally owned and ghosted elements. Locally accumulate nodal volume field followed by a copy owned to shared.
P1
P0
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
edge 1
edge 2
face 1

## Slide 17: Parallel Strategies: Option 1
Sierra Toolkit/Standard Ownership rules: Mesh object (nodes, edges, faces, elements) owned by lower-rank. For example:
P0 locally owns E1 and nodes 1, 2, 4, and 5
P1 locally owns E2, E3, and E4 and nodes 3, 6, 7, 8, and 9
P0 and P1 share nodes 2, 4, and 5
Desired Control-Volume Finite Element (CVFEM) Operation:
“nodal volume” assemble for node 5 via iteration of each 1cmx1cm element. Desired nodal volume for node 5 = 1 cm2 exactly the same on both parallel ranks
Options:
1. Iterate over locally owned elements and locally accumulate nodal volume field followed by a parallel sum and copy owned to shared.
2. Ghost element E2, E3, and E4 to P0 and E1 to P1 (along with coordinates) and iterate locally owned and ghosted elements. Locally accumulate nodal volume field followed by a copy owned to shared.
P1
P0
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
edge 1
edge 2
face 1
¼
¼
¼
¼

## Slide 18: Parallel Strategies: Option 2, A View from P0
P1
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
Ghost P1 -> P0
P0
All work performed on P0
Ghosting and communication required
No parallel sum (think about a matrix entry)

## Slide 19: Parallel Strategies: Option 2, A View from P1
P0
P1
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
Ghost P0 -> P1
All work performed on P1
Ghosting and communication required
No parallel sum (think about a matrix entry)

## Slide 20: Conceptual Disparity Between Low- and High-Order
Recall, that for unstructured schemes, increased connectivity to achieve a higher-order basis is difficult
However, we have discussed a notion of “polynomial promotion” of the underlying basis that provides higher-order convergence
Spectral convergence
Dual-volume for promoted quad4

## Slide 21: Work!
Obviously, the promoted element has far more nodes
Gauss-Lobatto: nodes
Gauss-Legendre: sub-control surfaces
Rotating cube (Re 4000, RPM 3600) P=1 (top) and P=2 (bottom)

## Slide 22: Timely Publications on Next Generation Platforms
Knaus, Robert. 2022. “A Fast Matrix-Free Approach to the High-Order Control Volume Finite Element Method with Application to Low-Mach Flow.” Computers & Fluids, https://doi.org/10.1016/j.compfluid.2022.105408

## Slide 23: High Performance Computing for CFD: Conclusions
Several fluids applications found in the low-Mach application space require HPC
Strong and weak scaling are of interest in engineering analysis
Communication bottlenecks can affect scaling
From a user-perspective, scaling is critical to efficiently deploying production simulation results
Path towards NGP will require disruptive technology with significant code investments