## Slide 1: ME469: Mesh Motion Approaches
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Thus Far, Many Complex Applications: Multi-physics, Static-Mesh

## Slide 3: However, Many Applications in Which A Body Moves…..
Wave, Coe et al., SAND2016-10094
Wind, Sandia SWIFT facility,
https://energy.sandia.gov
https://web.stanford.edu/group/frg/

## Slide 4: Moving Mesh Approaches
Options: mesh deformation, sliding mesh and overset

## Slide 5: Mesh Deformation and Mesh Smoothing
The mesh remains conformal and distorts (compresses and is stretched) as the solid body moves.
Elements encounter a volumetric time-rate of change
Flow past an erratic airfoil

## Slide 6: A Note on Fluid/Structure Interaction (FSI)
FSI drives coupling between the solid body structural response, the fluid mechanics (force and loadings), and the mesh smoothing scheme
Wave Generator
Linear Elastic Structural Mechanics
Fluids solve provides static n1/2 pressure (surface)
Info:
density (top; water is blue)
static pressure (bottom)
– roughly ten seconds

## Slide 7: A Note on Fluid/Structure Interaction (FSI)
FSI drives coupling between the solid body structural response, the fluid mechanics (force and loadings), and the mesh smoothing scheme
Wave Generator
Linear Elastic Structural Mechanics
Fluids solve provides static n1/2 pressure (surface)
Mesh Motion Mechanics
SM solve provides displacements (surface)
Lame’ constants
Info:
density (top; water is blue)
static pressure (bottom)
– roughly ten seconds
PDE-based where stress is modeled (above elastic) with special properties

## Slide 8: A Note on Fluid/Structure Interaction (FSI)
FSI drives coupling between the solid body structural response, the fluid mechanics (force and loadings), and the mesh smoothing scheme
Wave Generator
Linear Elastic Structural Mechanics
Fluids solve provides static n1/2 pressure (surface)
Mesh Motion Mechanics
SM solve provides displacements (surface)
Lame’ constants
Info:
density (top; water is blue)
static pressure (bottom)
– roughly ten seconds
Smith et al. “Stable Neo-Hookean Flesh Simulation”, Pixar Animation Studios,
and “spring” approaches that connect opposing vertices of the element

## Slide 9: Physical Analogy: Model the mesh by connected springs
Rather than solve a PDE with a modified stress model, the elements can be tied together by “springs”, see Yang et al, “Improvement in the spring analogy mesh deformation method through the cell-center concept”, Aero. Science Tech. (2021)
  Physics Analogy (as apposed to PDE-based)

## Slide 10: A Note on Fluid/Structure Interaction (FSI)
FSI drives coupling between the solid body structural response, the fluid mechanics (force and loadings), and the mesh smoothing scheme
Wave Generator
Linear Elastic Structural Mechanics
Fluids solve provides static n1/2 pressure (surface)
Mesh Motion Mechanics
SM solve provides displacements (surface)
Lame’ constants
Fluid Mechanics
MM solve provides velocity (surface and volume) and displacements (volume)
r
Info:
density (top; water is blue)
static pressure (bottom)
– roughly ten seconds

## Slide 11: Geometric Conservative Law (GCL)
For moving mesh applications, care must be taken such that a moving mesh does not create spurious flow
The Geometric Conservative Law states, simply, (below V is the volume, and vj is the mesh velocity):
The conservation equation for scalar f is
In general, CGL does not come for free and there are varying levels of sophistication that one can employ:
  Discrete–GCL, Guillard and Farhat, Comput. Method. App;. Mech. Engr. 190 (2000)
  “Geometry Correction” Ma et al., Proc. Engr. 126 (2015)
  Lineage from Arbitrary Lagrangian Eulerian (ALE)

## Slide 12: Complexity: Mesh Inversion
In general, there may be a maximum mesh displacement that can not be supported

## Slide 13: Sliding Mesh: Conceptual Description: Review
A generalized non-conformal scheme supports will fixed rotation
Conceptually, multiple sliding blocks can be included
Below, we note:
  Front blade, COUNTER-CLOCKWISE
  Back blade, CLOCKWISE

## Slide 14: Multiple Sliding Mesh: Geometry

## Slide 15: Halo-based Approach for Non-Conformal Interfaces: Vertex-Based
Has the “flavor” of an overset method; i.e., extrusion of surface mesh to opposing domain with reconstruction of states
Two-pass algorithm: surface_1:block_2 and surface_2:block_1
See Stejil, 2008 and extrusion-based of Blades, 2006 and Dodds, 2016
First implemented in Nalu for wind-energy applications, Domino, JCP 2018
Requires prescribed movement, e.g., VAWT

## Slide 16: Halo-based Approach for Non-Conformal Interfaces; CC-based
Has the “flavor” of an overset method; i.e., extrusion of surface mesh to opposing domain with reconstruction of states
Two-pass algorithm: surface_1:block_2 and surface_2:block_1
See Stejil, 2008 and extrusion-based of Blades, 2006 and Dodds, 2016
First implemented in Nalu for wind-energy applications, Domino, JCP 2018
Requires prescribed movement

## Slide 17: Design-order Mesh Constructs for Non-Conformal Interfaces: Requires Prescribed Mesh Movement
Non-conformal and overset methods provides ease of meshing and, when required, mesh motion
Design-order hybrid DG/CVFEM established, see Domino, J. Comput. Phys. (2018) based on classic discontinuous Galerkin work of Arnold et al. SIAM (2002)
Non-conformal MMS
Current/Opposite

## Slide 18: Shock Tube: Non-conformal Mesh
Hybrid DG/CVFEM-based non-conformal algorithm originally developed for the low-Mach regime
Domino, S. P., "Design-order, non-conformal low-Mach fluid algorithms using a hybrid CVFEM/DG approach", J. Comput. Physics, 2018,
  https://doi.org/10.1016/j.jcp.2018.01.00
Compressible AUSM regime
Non-conformal (static) interface
New!

## Slide 19: What is there is non-prescribed mesh motion?
In many applications, the movement of the body is coupled to the fluid flow
What then?
Buoy drop of Ransley et al., Renew. Ener. (2017)
Falling/rising sphere of Horne and Mahesh, J.
Comput. Fluids, (2019)

## Slide 20: Overset!
Background and overset meshes are defined

## Slide 21: Overset: Freedom for Generalized Motion
Implicit, constraint-based overset-based approach, AKA, Chimera”, Chesshire and Henshaw, J. Comput. Phys. 90 (1990)
Does not require presumed movement
Similar to Sharma et al, J. Comput. Phys. (2021), however, STK-based search
BLOCK_2
BLOCK_1
BLOCK_3 (newly declared and
changed part)
Surface_101 (newly declared and changed part)
Surface_1 (read in)
Fluids Hex/Tet
MMS
Constraint-based

## Slide 22: Overset: Freedom for Generalized Motion
Implicit, constraint-based overset-based approach, AKA, Chimera”, Chesshire and Henshaw, J. Comput. Phys. 90 (1990)
Does not require presumed movement
Similar to Sharma et al, J. Comput. Phys. (2021), however, STK-based search
BLOCK_2
BLOCK_1
BLOCK_3 (newly declared and
changed part)
Surface_101 (newly declared and changed part)
Surface_1 (read in)
Fluids Hex/Tet
MMS
Constraint-based
Fringe

## Slide 23: Shock Tube: Overset Mesh
Based on implicit constraint-based approach originally developed for the low-Mach regime
Domino, S. P. and Horne, W., "Development and deployment of a credible unstructured, six-DOF, implicit low-Mach overset high-fidelity simulation tool for wave energy applications”, submitted to Renewable Energy (11/2021)
Extended to compressible regime
Overset (static) interface
New!

## Slide 24: Buoy Subjected to large Wave-Form Validation Benchmark: Explore Center of Mass
Low COM
High COM

## Slide 25: Mesh Motion Review
Low-to-Moderate Displacement:
Solid mechanics analogies, either PDE or physical (springs)
Added GCL requirements, matrix is constant
Prescribed Mesh Motion via sliding:
Halo, or DG-based
No added GCL, however, matrix changes (along well-defined surfaces)
Full six-DOF motion:
Overset
Everything changes!