## Slide 1: ME469: Nalu Overview
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Lecture Objectives
Nalu Technology Origination: Advanced Simulation and Computing project (NNSA)
Beyond the 32-bit Limit
Supported Physics
Supported Numerics
Low- and High-order
Moving Mesh (Sliding and Overset)
Multiphysics
  Fluid Structure Interaction
  Conjugate Heat Transfer (CHT)
  Participating Media Radiation
  Examples

## Slide 3: Core Technology Provided to Nalu Origination: Advanced Simulation and Computing Sierra/Fuego
Use-case characterized by a highly sooting, turbulent, reacting flow with Participating Media Radiation (PMR), Conjugate Heat Transfer (CHT), and propellant multi-physics coupling
Complex geometry has driven a generalized, hybrid unstructured discretization approach supporting Hex8, Tet4, Wedge6, and Pyramid5 elements in addition to promotion of Hex8 to Hex27, and Tet4 to Tet10

## Slide 4: Goal: Beyond 32-bit Computing
Circa 2013, many scientific production codes were limited to 32-bit
Therefore, maximum simulation size for entities, e.g., node, edge, face, element, etc., was ~2.2 billion
Next Generation Platforms were advocated to overcome poor MPI scaling and power needs to support Exascale computing (1018 floating point operations/second)
  Platform architectures, at that point, were not not yet known (still evolving)
( )
Sierra Toolkit/Trilinos (open-source)
MPI+X parallelism
Support for new architectures
+ ASC Investments

## Slide 5: Developed Open-Source BSD-clause 3 Distribution Policy
Philosophy: Open-source collaborations
https://github.com/NaluCFD

## Slide 6: Supported Physics: DNS and LES (even RANS)

## Slide 7: A Note on High Performance Computing
Sandia (and Stanford) are committed to High Performance Computing (HPC) to support is science and engineering objectives: Exercised herein
O(6) billion wind energy application
O(2) billion DNS impinging jet
O(200) million multi-physics fire

## Slide 8: Nalu Timeline/History
By CFD standards, this is a relatively new code base
Sierra/Nalu
SNL License
Github
Nalu
Open-source
BSD License (2014)
Active
academic partners
Github
Nalu-Wind
ECP ExaWind (2018)
Open-source: SNL, NREL, ORNL, UT joint copyright
…. etc

## Slide 9: Several Multi-physics Flow Examples From Nalu
Impinging Jet DNS
Cylinder in cross flow
Whirling behavior
Helium plume (low-/high-order)
Heated backstep

## Slide 10: Nalu Abstractions: Polymorphic and Input File-Driven
Domain
Time Integration
Realm B
Realm A
1 to many
boundary
algorithms
1 to many
Interior
algorithms
Transfer
1 to many
boundary
algorithms
1 to many
Interior
algorithms
Nonlinear Coupling
Operator-split multi-physics
Conjugate heat transfer coupling
Fluids Realm
Heat Conduction Realm
Realm specifications define the physics and desired boundary conditions
Pre-defined EquationSystems (segregated or monolithic)
Operator-split multi-physics:
Conjugate heat transfer coupling
  Fluids and solid Realm

## Slide 11: Essential Attributes of a CFD Simulation
Mapping from Real World, to Conceptual Model, and, finally, a Computer Model (given an underlying PDE discretization approach)
mesh: my_mesh.g
euations: my_equations
- inflow_boundary_condition: bc_left
target_name: Inflow
velocity: [1.0,0.0]
mixture_fraction: 0.0
Mesh
Input File(s)
Hex8
Tet4
launch remotely
Remote Viz
output.log
output.e.32.*
output.rst.32.*
>scp output.e.32.* /to/my/local/disk
launch locally

## Slide 12: 30K View: Anatomy of a Nalu Input File:YAML-based
Simulation:
linear_solvers:
transfers:
realms:
- name: realm_heatCond
boundary_conditions:
- wall_boundary_condition: bc_exposed
solution_options:
initial_conditions:
material_properties:
equation_systems:
systems:
- HeatConduction:
output:
restart:
- name: realm_fluids
TimeIntegrators:
Specification of sparse Trilinos-based precond/solver
Data transfer for multi-physics coupling
Physics definitions
Time integration, e.g., BE, BDF2
YAML enforces strict spacing and ordering
https://www.democraticunderground.com/10021540110

## Slide 13: High-Level Elements of an Input File
systems:
- LowMachEOM:
name: myLowMach
- MixtureFraction:
name: myZ
initial_conditions:
- constant: ic_1
target_name: [block_1, …]
value:
pressure: 0
velocity: [0.5,0.0]
mixture_fraction: 0.0
material_properties:
target_name: block_1
specifications:
- name: density
type: constant
value: 1.0
- name: viscosity
type: constant
value: 1.8e-5
boundary_conditions:
- inflow_boundary_condition: bc_left_inflow
- wall_boundary_condition: bc_front_wall
- open_boundary_condition: bc_right_open
- symmetry_boundary_condition: bc_top
- nonconformal_boundary_condition: bc_nc
- inflow_boundary_condition: bc_left
target_name: surface_1
inflow_user_data:
velocity: [0.5,0.0,0.0]
mixture_fraction: 0.0
material_properties:
target_name: block_1
specifications:
- name: density
type: ideal_gas
- name: viscosity
type: polynomial
coefficient_declaration:
- wall_boundary_condition: bc_back
target_name: surface_7
wall_user_data:
user_function_name:
velocity: wind_energy
user_function_string_parameters:
velocity: [mmTop_ss7]
mixture_fraction: 1.0

## Slide 14: A Note on Parallel Decomposition
Decomposing the mesh into small subsets and operating on these subsets in parallel provides a methodology for increased simulation time
Colored by block ID
Colored by core count (= 1) One mpi rank. 16 MPI ranks = 16x faster (hopefully)

## Slide 15: How to Run in Parallel: Mesh Decomposition
Given a mesh, mesh.g and myInputFile.i, if one desires to run on, e.g., 16 core case:
  Use pre-processing “decomposition” tools (Trilinos/install/bin)
  In-situ decomposition
- name: realmFluids
mesh: mesh/myMesh.g
automatic_decomposition_type: rcb
myMesh.g
- name: realmFluids
mesh: mesh/myMesh.g
automatic_decomposition_type: rcb
>/path/to/decomp –j {np} {meshName}
>mesh.g.16.00, mesh.g.16.01, .., mesh.g.16.15
>results.e.16.00, results.e.16.01, .., results.e.16.15
>input.log
2:
1:
>mpirun --np 16 /naluPath/naluX -i input.i &

## Slide 16: A Note on Divergence
Whether by design or poor code usage, solution results from CFD analysis for complex applications may diverge. How do I know?
Non-finite residuals, i.e., not-a-number:“nan” (either linear or non-linear),
  const double norm = 0.0;
  const double flux = rho*u*A/norm;
What if the simulation runs, however, results look very wrong? Typical causes?
  Bad initial condition that drives nonlinear solution to diverge
  Too large of an initial time step
  Poor stabilization, numerical parameters, etc.
  Poor time integration
  Ph.D. from ICME explaining why…
EBVC flow-past 2D cylinder
Top: +NOC
Bottom se: -NOC

## Slide 17: Test Case Input Files
  Input files are part of the Nalu regression test suite: Nalu/reg_test/test_files
  Mesh files are found under: Nalu/reg_test/mesh
  Formally, /mesh is a git submodule
  Test Cases Highlighted:
  Nalu/reg_tests/test_files/dgNonConformalThreeBlade
  Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Resource: https://nalu.readthedocs.io/en/latest/source/theory/index.html

## Slide 18: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Physics:
  Flow past rotating square blades (Re = 10,000)
Models
  Newtonian fluid (air) with constant properties
Boundary Conditions
  Inflow, open, symmetry, DG/CVFEM interface
>mpirun --np 4 /naluPath/naluX -i dgNonConformalThreeBlade.i &
Domino, JCP, 2018

## Slide 19: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
gi for BDF2
UDt/Dx
r U L / m
Nonlinear
iterations
Equations
Review

## Slide 20: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Physics:
  Uniformly emitting/absorbing participating media radiation (PMR) conjugate heat transfer (CHT) with buoyancy
Models:
  Newtonian fluid (air): ideal gas
Boundary Conditions:
  Wall, periodic
>mpirun --np 8 /naluPath/naluX -i fluidsPmrChtPeriodic.i &
Stark#, cond/rad
Sk = l m / s Ti3 ~ 0.4
Rayleigh#, tThermalDiff/ tConv
Ra = g b (Ti – To ) L / Pr a2 ~ 2e6

## Slide 21: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Temperature
Irradiation
Participating
Media
Radiation DOM
STK
Transfer
VOLUME
SURFACE
Δ
۰qr
Temperature, mg
RTE Src
Linearized
Temperature
Convection Coef.
Reference Temp
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
Turbulent
Fluid Mechanics,
Combustion
Monolithic, i.e., fully coupled, approaches are intractable due to the size of (u, v, w, p, h, hr, Z, Ik T)T
Stable and accurate operator split methods are, therefore, sought
  See Domino et al., AIAA, 2007

## Slide 22: Break-out Example Using Paraview
Live demo