## Slide 1: ME469: Numerical Abstractions
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Useful Abstractions
The intended application
Physical laws, hypothesis and models (e.g. a set of PDEs) and initial and boundary conditions
A set of computational algorithms that allow to build a numerical, or approximated solution to the conceptual model
Real World
Conceptual
Model
Computer Model

## Slide 3: Mappings:
Real World
Conceptual
Model
Computer Model
?

## Slide 4: Qualification: Adequacy of the conceptual model to provide an acceptable level of agreement for the intended application
Real World
Conceptual
Model
Computer Model
Examples:
Is the fluid Newtonian?
Are compressibility effects important?
Uniform or variable-density?
Isothermal or non-isothermal?

## Slide 5
Real World
Conceptual
Model
Computer Model
Examples:
Is it RHS += A, RHS -=A? Which is correct?
Should the contribution be scaled by a volume?
How does the Quantity of Interest (QoI) behave as a function of mesh or time step resolution?
Verification: Process of determining that (1) the model implementation faithfully represents the conceptual model (without mistakes) and (2) the solution to the model is accurate
Verification

## Slide 6
Real World
Conceptual
Model
Computer Model
Examples:
Midterm project: compare drag coefficient prediction to an experiment
Final project: compare drag coefficient for flow past rotating shapes; chaotic flow prediction at a given configuration
Validation: Process of determining the degree to which the numerical solutions (hence the model) is an accurate representation of reality from the perspective of the intended application
Validation

## Slide 7: Verification vs Validation (V&V)? The Formal Lexicon
Verification: Are we solving the equations correctly?
Represents an exercise in computational mathematics
Given an equation, is the solution converging at known rates?
Validation: Are we solving the correct equations?
Represents an exercise in understanding the physics associated with the real world use case
In this course, we will strongly focus on verification
Establishing the correctness of the numerical implementation is key
Comparisons of the numerical results to reality is not the primary objective
Verification challenges?
Knowledge of the true solution, i.e., exact analytical solutions
How many exact solutions exist for our class of physics? Not many!
Hint: Method of Manufactured Solutions (MMS)

## Slide 8: The Construction of a Numerical Method: Discretization and Solution
Real World
Conceptual
Model
Computer Model
Mathematical Formulation
Partial differential equations (PDE)
Initial Conditions (IC)
Boundary Conditions (BC)

## Slide 9: The Construction of a Numerical Method: Discretization and Solution
Real World
Conceptual
Model
Computer Model
Mathematical Formulation
Partial differential equations (PDE)
Initial Conditions (IC)
Boundary Conditions (BC)
Discretization step
Numerical Formulation
Discretize in space and time
Algebraic Differential Equations (ADE)

## Slide 10: The Construction of a Numerical Method: Discretization and Solution
!Real World
Conceptual
Model
Computer Model
Mathematical Formulation
Partial differential equations (PDE)
Initial Conditions (IC)
Boundary Conditions (BC)
Discretization step
Numerical Formulation
Discretize in space and time
Algebraic Differential Equations (ADE)
Solution step
Numerical Solution
Algebraic Differential Equations (ADE)
Linear solvers
Convergence, mesh adequacy, ….?

## Slide 11: Numerical Simulation Conundrum
What we would like to have…
PDE
Exact
Solution

## Slide 12: Numerical Simulation Conundrum
What we would like to have…
PDE
Exact
Solution
What we have….
ADE
Numerical
Solution

## Slide 13: Numerical Simulation Conundrum
What we would like to have…
PDE
Exact
Solution
What we have….
ADE
Numerical
Solution
?
Need to relate the numerical solution of the discretized problem to the exact solution of the original continuous problem!

## Slide 14: Numerical Simulation Conundrum
For a well-posed, linear PDE, Lax-Richtmyer Equivalence Theorem, AKA the Fundamental Theorem of Numerical Analysis: Consistency + Stability = Convergence
PDE
Exact
Solution
ADE
Numerical
Solution
Consistency
Convergence
Stability

## Slide 15: Example 1: Vortex Street
Real World?
Conceptual
Model
Computer Model

## Slide 16: Example 2: Modeling a Luminaria – In the Snow!
Real World?
Conceptual
Model
Computer Model