## Slide 1: ME469: Residual-based Advection Stabilization
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Review of Advection Stabilization Options
For the high Peclet number use case, on unstructured meshes, we have identified three strategies:
Ad hoc blending between upwind and central using an indicator that is a function of cell Peclet number:
Gradient reconstruction (upwind) approaches with limiters
Monotonic upstream-centered scheme for conservation laws (MUSCL) - again, with limiters

## Slide 3: Momentum Field is Tolerant of low-Dissipation Advection Operators
…. While passive scalars are not

## Slide 4: Re = 2000 (local Re 20) – No Stabilization
Analytical solution from Mojtabi and Deville, One-dimensional linear advection–diffusion equation: Analytical and finite element solutions, Comput. Fluids 107 (2015) 189–195.
Linear Basis (CVFEM), central/Galerkin
Quadratic Basis (CVFEM), central/Galerkin

## Slide 5: Re = 2000 (local Re 20) – Upwind
Analytical solution from Mojtabi and Deville, One-dimensional linear advection–diffusion equation: Analytical and finite element solutions, Comput. Fluids 107 (2015) 189–195.
First-order upwind
Second-order upwind
Second-order upwind + limiter

## Slide 6: Recall a Strategy: Central + Diffusion
A general advection system can be written in terms of a central-based scheme and a diffusion term using an effective viscosity
The goals are to be:
Consistent, i.e., as you refine the mesh, you revert to the desired PDE
Design-order, i.e., converges as Dxp+1
Simply re-casting a first-order upwind scheme
Lax-Wendroff, System of
Conservation Laws, LA-2285 (1960)
Similar to Taylor-Galerkin

## Slide 7: Residual Definition
On a given mesh, h, if we were to evaluate the residual, what would we obtain?
As we refine the mesh, the evaluation of this “fine-scale” residual would approach zero – at least for a consistent discretization approach whose truncation error is well-behaved
A classic residual-based stabilization, Streamwise Upwind Petrov-Galerkin (Hughes and Brooks, 1982) – more generalized within the Variational Multiscale Method (VMS, Hughes et. al, 1998)
Element-metrics
b ~ 1; c ~ O(10)

## Slide 8: SUPG Stabilization in a Finite Volume Context
Finite Element Context:
Finite Volume Context by applying the piecewise constant test function:
Assuming we have a design-order representation of the residual, the method is consistent
With:
Note: Godunuv’s theorem states that a
linear stabilization approach is not
sufficient to damp out all oscillations

## Slide 9: SUPG Stabilization in a Finite Volume Context
Finite Element Context:
Finite Volume Context by applying the piecewise constant test function:
Assuming we have a design-order representation of the residual, the method is consistent
Note: Diffusion terms, a second-order derivative require special care (projection)
With:
Note: Godunuv’s theorem states that a
linear stabilization approach is not
sufficient to damp out all oscillations

## Slide 10: Linear Residual-Based Stabilization: CVFEM closer look
For now, let’s remove time, diffusion and source – and assume density and velocity are constant
Recall central and upwind stencils for our standard 1D configuration (flow left to right)
General interpretation: looks like diffusion with coefficient, , where is a flow-aligned time scale (s)
If we allow Let , then we recover upwind!
In general, the key is to include the full PDE residual
j-1
j
j+1
Zj+1/2
Zj-1/2
A

## Slide 11: Linear Residual-Based Stabilization: Consistency
The residual-based stabilization is given by,
with the fine-scale residual defined as,
Comments:
If the fine-scale residual is consistently evaluated, then as the mesh is refined the residual-based stabilization is removed
Recall that this is a linear stabilization scheme and may still admit oscillations
In the pure Finite Element Method description, this form of stabilization is a Petrov-Galerkin approach

## Slide 12: SUPG in Practice (CVFEM and FEM)
SUPG and the analog in CVFEM, Streamwise Upwind Control Volume (SUCV) are effective for low-moderate cell-Peclet numbers
Un-stabilized and SUPG
Convecting TV
SUPG/SUCV (Aria, hfem; Aria cvfem) back step
velocity prediction compared to upwind (Fuego)

## Slide 13: SUCV Generalized to Other Systems
Recall the radiative transport equation – derived in a variational multiscale (VMS) context, Domino et al., Phys. Fluids (2021)
a = b = 0, SUCV!

## Slide 14: Nonlinear Stabilization Operator (NSO)
An artificial viscosity approach is provided with coefficient again related to a fine-scale residual, shown for both finite element and finite volume:
Here, we link the artificial diffusion coefficient to the fine scale residual:
                Or min of::
Origin from FEM-based discontinuity capturing operator (DCO), Shakib et al. Comput. Method. Appl. Mech. Engr., (1991)
Similar concept to Guermond et al. “Entropy-viscosity” approach, J. Comp. Phys. (2011)
  Variations form an interesting LES subgrid model when the viscosity is a function of the k.e. fine scale residual (Guermond and Larios, 2015)

## Slide 15: Re = 2000 (local Re 20) – Residual-Based
Analytical solution from Mojtabi and Deville, One-dimensional linear advection–diffusion equation: Analytical and finite element solutions, Comput. Fluids 107 (2015) 189–195.
NSO, linear basis (CVFEM)
NSO, quadratic basis (CVFEM)
SUCV, linear basis (CVFEM)

## Slide 16: Now, Direct Comparisons, Order of Accuracy
Convecting Taylor/Vortex simulation at high crossflow velocity
Results demonstrate the ability to deploy this stabilization approach to high-order