## Slide 1: ME469: Multiphase Methods: Volume of Fluid Methods
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Objective: Model Multiphase Flow (Air/Water)
Validation case of Kleefsman et al. ”A volume-of-fluid based simulation method for wave impact problems”, J. Comput. Phys. (2005).
See:
/laboratory/3d_hex8_dam_break

## Slide 3: Step 1: Definition of an Water/Air interface (Phase 1/Phase 2)
Signed-distance function (level-set), Y
Popularized by Osher and Sethian, “Fronts propagating with curvature-dependent speed: Algorithms based on Hamilton-Jacobi formulations”, J. Comp. Phys., 1988,
Volume of Fluid, f or a
Lineage classically provided to Noh, W.F.; Woodward, P. (1976). van de Vooren, A.I.; Zandbergen, P.J. (eds.). SLIC (Simple Line Interface Calculation). proceedings of 5th International Conference of Fluid Dynamics. Lecture Notes in Physics. Vol. 59. pp. 330–340
Interpretation: volume fraction of phase 1, interphase lives at ½
defines an zero-isocontour, with distance
(+/- in either direction)
Interface normal and curvature

## Slide 4: Definition of an Water/Air interface (Phase 1/Phase 2)
Signed-distance function (level-set), Y
Popularized by Osher and Sethian, “Fronts propagating with curvature-dependent speed: Algorithms based on Hamilton-Jacobi formulations”, J. Comp. Phys., 1988,
Volume of Fluid, f or a
Lineage classically provided to Noh, W.F.; Woodward, P. (1976). van de Vooren, A.I.; Zandbergen, P.J. (eds.). SLIC (Simple Line Interface Calculation). proceedings of 5th International Conference of Fluid Dynamics. Lecture Notes in Physics. Vol. 59. pp. 330–340
Interpretation: volume fraction of phase 1, interphase lives at ½
defines an zero-isocontour, with distance
(+/- in either direction)
Interface normal and curvature

## Slide 5: VOF Transport Discretization Nuance: Volume- or Surface-based?
Simple enough, define the volume (fraction) of fluid (absent evaporation):
Option 1: volumetric-form:
Option 2: divergence-form:
CVFEM/FEM (really, any element-based approach)
Evaluated as a volumetric-contribution (diamonds)
Traditional finite volume (element, edge, cell-centered)
Evaluated as a surface integral (triangle)
Allows for a consistent advecting velocity (mass conserving)
that is obtained from the continuity equation
Gauss-Divergence

## Slide 6: Baseline: Generalized, Unstructured Numerical Formulation
Objective: Scalable, Efficient fluids on hybrid-based mesh constructs
Rotating cube (Re 4000, RPM 3600)
P=1 (top) and P=2 (bottom)
Control-volume finite-element method (CVFEM)
CVFEM can be viewed as Petrov-Galerkin method (basis differs from test function)
High-quality on generalized unstructured meshes, Domino et al. Comput. Fluids (2019)
The method can also be promoted in polynomial space, see Domino, CTRSP (2014) as a first example of low-Mach fluids algorithm – or Domino, J. Comp. Phys. (2018)
  GPU, Knaus, Comput. Fluids (2022)

## Slide 7: Equal-Order Interpolation, i.e., Collocation: Pressure Stabilization Review (1/2)
A variety of forms/explanations – depending on the particular community; at it’s base:
What is ? (next slide)?
Projected nodal gradient that
can be mass-lumped

## Slide 8: Equal-Order Interpolation, i.e., Collocation: Pressure Stabilization Review (2/2)
is a function of the fine-scale momentum residual (evaluated at an integration point):
We can also project this residual to the nodes, and approximate Rh(uj) as re-interpolation of choice terms
Usage of a full residual (1) results in a classic Pressure Stabilized Petrov Galerkin (Hughes et al. 1986)
Pick and choose each residual, Majumdar (1988)
Algebraically manipulation affords the classic Rhie-Chow-based (1983) pressure stabilization
- shown to be stable and dissipative [Ham and Iaccarino (2004) or Domino (2006)]
There is also the nuance of pressure projection vs monolithic
(1)

## Slide 9: VOF Transport: Sharpening + Advection Stabilization + Interface Smoothing
VOF equation with PDE-based sharpening (to mitigate numerical diffusion) that includes residual-based stabilization
PDE-based sharpening with compression velocity
in the direction of the interface normal,
Streamwise-upwind, control volume (SUCV), Swaminanthan et al., Int. J. Numer.
Meth. Engr. (1993); based on Streamwise Upwind Petrov-Galerkin (SUPG),
Brooks and Hughes, Comput. Methods in Appl. Mech. Eng. (1982).
Nonlinear stabilization operator (NSO); Motivated by Shakib et. al, Comput.
Methods in Appl. Mech. Eng. (1991), discontinuity capturing operator
(later termed NSO); nh = f(Rh(a)) NSO and SUCV avoids common gradient
reconstruction techniques commonly used in unstructured formulations, see
Tsui et al., Int. J. Heat Mass Trans. (2009)
Nuance: interface normal can be computed using a smoothed VOF field
Integrated-by-parts advection to allow for consistent continuity constraint; Rh(a)

## Slide 10: VOF using Balanced Force: Brief Survey
First CVFEM: Lin et al, J. Comput. Phys. (2019)
Classic Balanced Force, Francois, J. Comput. Phys. (2006) ported to CVFEM
Parasitic currents suppressed via a consistent momentum/continuity stabilization form: fine-scale momentum residual algebraically modified in continuity equation
  Note: not trying to pioneer a novel balanced force approach
Note: benefits from rgi (g = 1) included in stabilization
Momentum Equation
Continuity Equation
Convecting-velocity
Nodal pressure gradient

## Slide 11: VOF using Balanced Force: Leveraging Existing Approaches
First CVFEM: Lin et al, J. Comput. Phys. (2019)
Classic Balanced Force, Francois, J. Comput. Phys. (2006) ported to CVFEM
Parasitic currents suppressed via a consistent momentum/continuity stabilization form: fine-scale momentum residual algebraically modified in continuity equation
  Note: not trying to pioneer a novel balanced force approach
Note: benefits from rgi (g = 1) included in stabilization
Momentum Equation
Continuity Equation
Surface tension Continuum Surface Force (CSF)

## Slide 12: A Note on Methods and CSF
Many (local!!) experts:
Jain et al., A conservative diffuse-interface method for compressible two-phase flows, J. Comp. Phys, 2020.
Jain, “Accurate conservative phase-field method for simulation of two-phase flows, J. Comp. Phys, 2022.
Mirjalili et al., Assessment of an energy-based surface tension model for simulation of two-phase flows using second-order phase field methods, J. Comp. Phys. 2023.
Huang and Jain, “A phase-filed method for simulations of two-phase flows on unstructured grids”, Annual CTR Briefs, 2022.
Barbeau and Lele, Assessment of Localized Artificial Diffusivity (LAD) and Interface Sharpening for Modelling a Two-Phase Mixing Layer, PSAAP-3 Poster Session.

## Slide 13: Passive Transport Example: Driven Cavity
Exploring PDE-based sharpening, interface smoothing and stabilization
A B C
D E F
Initial condition
No stabilization
SUCV+NSO
Sharpening+B
Sharpen+C
E+Smoothing

## Slide 14: Residual-based stabilization
Molenkamp verification, see Martinez, Int. J. Numer. Meth. Engr. (2004), with a variety of stabilization options
First-order, upwind (FOUPW)
Second-order, UPW+Limit (SOUPW, limit)
SUCV, Polynomial-order = 1
SUCV, Polynomial-order = 2
Conformal mesh results
(stay tuned for overset)

## Slide 15: Dam Break Validation: The Benefit of a Full Balanced-Force Method
Here, comparisons made between g = 1 (top) and g = 0 (bottom) showcasing the increased stabilizing effect of the set of all body forces in momentum included in the pressure stabilization formulation
A nuance briefly captured and/or hinted at in seminal Francois et al., J. Comput. Phys. (2006) effort
R0

## Slide 16: Dam Break Validation: The Benefit of a Full Balanced-Force Method
Here, comparisons made between g = 1 (top) and g = 0 (bottom) showcasing the increased stabilizing effect of the set of all body forces in momentum included in the pressure stabilization formulation
A nuance briefly captured and/or hinted at in seminal Francois et al., J. Comput. Phys. (2006) effort
R2

## Slide 17: Dam Break Validation
Validation case of Kleefsman et al. ”A volume-of-fluid based simulation method for wave impact problems”, J. Comput. Phys. (2005).
Qualitative comparisons also made to SNL’s Sierra/Fuego, Brown et al. “Modeling a rubble fire consisting of comingled liquid and solid fuel”, Tech. Rep. SAND2017- 12318C (2017).
R0
R1
R2
H1
H2
H3

## Slide 18: Overset: Freedom for Generalized Motion
Implicit, constraint-based overset-based approach (DG/CVFEM-based, started)
Does not require presumed movement
Similar to Nalu-Wind’s Sharma et al, J. Comput. Phys. (2021), however, STK-based search
BLOCK_2
BLOCK_1
BLOCK_3 (newly declared and
changed part)
Surface_101 (newly declared and changed part)
Surface_1 (read in)
Fluids Hex/Tet
MMS
Constraint-based
Fringe

## Slide 19: Objective: Overset + Volume of Fluid (VOF)
Molenkamp verification case, now with overset
Static bubble (computed curvature)
Hex8, Tet4, and Hex8/Tet4 Balanced Force
static bubble; density ratio = 1000

## Slide 20: Validation: Unmoored Buoy Drop (Quiescent Conditions)
  Comparisons are made to experimental data from the UK Centre for Marine Energy Research (UKCMER) of the WEC vertical displacement given in Ransley et al., Renew. Ener. (2017) who exercised a mesh deformation construct
3 m
5 m
5 m
0.5 m
0.25 m
0.25 m

## Slide 21: Validation: Unmoored Buoy Drop (Quiescent Conditions)
  Objective: Compare to experimental dataset and demonstrate grid convergence
  Displaced buoy vertically; QoI: center of mass spatial location as a function of time
  Finding: Improved comparison over other works found in literature, e.g., WEC vertical displacement given in Ransley et al., Renew. Ener. (2017)
0.31 m

## Slide 22: Validation: Moored Buoy Drop (Quiescent Conditions)
0.31 m
k = 500 N/m spring force
  Objective: Compare to experimental dataset and demonstrate grid convergence – now tethered
  Displaced buoy vertically; QoI: center of mass spatial location as a function of time
  Similar Finding: Improved comparison over other works found in literature, e.g., WEC vertical displacement given in Ransley et al., Renew. Ener. (2017)

## Slide 23: Buoy Dropped Into Quiescent Pool; large displacement limit Validation Benchmark, Domino and Horne, Renew. Energy (2022)
Large-displacement sample case run that can serve as a numerical benchmark

## Slide 24: Buoy Subjected to large Wave-Form Validation Benchmark, Domino and Horne, Renew. Energy (2022)
Large-displacement sample case run that can serve as a numerical benchmark for the community; with and without mooring
Geometric center = f(t) relative to the tether’s mounting point

## Slide 25: Buoy Subjected to large Wave-Form Validation Benchmark: Without (left) and With (right) Mooring