## Slide 1: ME469: A Verification and Validation (V&V) Methodology
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Verification and Validation Objectives
Introduce and Discuss:
Elements of a Poor/High-Quality Verification Study
Elements of a Pool/High-Quality Validation Study
Overview of a Phenomena Identification Ranking Table (PIRT)
  Cast within a fire safety use case
Solution Verification
The Role of Code Verification, including the Method of Manufactured Solutions (MMS)
Code Verification: Value Proposition
Review

## Slide 3: Our Exemplar: Heat Transfer Mechanisms: Abnormal/Thermal Environment (ATE)
  Characterized by a highly sooting, turbulent reacting flow with participating media radiation (PMR) and conjugate heat transfer (CHT) multi-physics coupling
  Liquid fuels, e.g., JP-8, are common due to its usage in transportation, however, propellants (point-Lagrangian/Eulerian) and composite (heterogeneous combustion) also encompass the ATE
Anderson Air Force B-2 Accident (2/2008)
[1] https://en.wikipedia.org/wiki/2008_Andersen_Air_Force_Base_B-2_accident
Propellant upward burn

## Slide 4: Objective: Deploy a High-Fidelity Tool to Predict a Fire with External Flow Coupling
  Consider that we want to develop and deploy a foundational understanding in, e.g., fire physics and deploy a simulation tool to support production analysis
  Let us introduce the fire-environment with elements of the following physics:
    Chemical reactions, soot, buoyancy, turbulent fluid mechanics, thermal radiation heat transfer, convective heat transfer, object heat-up/response, and sometimes propellants
    As mixing increases, accurately capturing convective heat loads becomes important
    This perspective and definition defines our ”conceptual” model
Volume-rendered
mixture fraction

## Slide 5: Verification vs Validation (V&V)? The Formal Lexicon (REVIEW)
Verification: Are we solving the equations correctly?
Represents an exercise in computational mathematics
Given an equation, is the solution converging at known rates?
Validation: Are we solving the correct equations?
Represents an exercise in understanding the physics associated with the real world use case
In this course, we will strongly focus on verification
Establishing the correctness of the numerical implementation is key
Comparisons of the numerical results to reality is not the primary objective
Verification challenges?
Knowledge of the true solution, i.e., exact analytical solutions
How many exact solutions exist for our class of physics? Not many!
Hint: Method of Manufactured Solutions (MMS)

## Slide 6: Challenge: Understanding Errors….
One mesh, one model, unknown code/numerical pedigree…
We need to distinguish the types of errors:
  Model-form Error
  Discretization Error
  Code Error?
What credible scientific hypothesis can be tested in this context?
Heat flux to the cylinder
Volume-rendered temperature
Time-averaged heat flux to cylinder

## Slide 7: Does a Process Exist? Phenomenological Identification and Ranking Table (PIRT)
A Phenomenological Identification and Ranking Table (PIRT) is:
A process that defines 1) what you know, 2) what you think you know, and 3) what “you know not of”
Legacy to the United States Nuclear Regulatory Commission (NRC), “The Phenomena Identification and Ranking Table (PIRT) process is a systematic way of gathering information from experts on a specific concept, and ranking the importance of the information, in order to meet some decision-making objective” [1]
Extensively used in the planning of high-consequence mod/sim/exp plans
[1] “Quantifying Reactor Safety Margins: Application of CSAU to a LBLOCA,” B.E. Boyack, et al, Part 1: An overview of the CSAU Evaluation Methodology; G.E. Wilson et al., Part 2: Characterization of Important Contributors to Uncertainty, W. Wulff et al., Part 3: Assessment and Ranging Parameters; C.S. Lellouche et al., Part 4: Uncertainty Evaluation of analysis Based on TRAC-PF1/MOD1; N. Zuber et al., Part 5: Evaluation of Scale-up Capabilities of Best Estimate Codes; I. Catton et al., Part 6: A Physically Based Method of Estimating PWR LBLOCA PCT, Nuclear Engineering and Design 119 (1) pp 1-117, May 1990.

## Slide 8: Step 1: Phenomena Identification and Ranking Table (PIRT)
  Identify all salient physics and rate the following:
  The importance of the phenomenon
  Adequacy of Models
  Adequacy of Code (does the code have the required models; has the code been “verified”)
  Adequacy of Validation (do we believe that the models capture the physical world)
  Once a particular use-case is understood and a PIRT is complete, one can proceed down the path of simply closing the gaps in the modeling, code implementation, and model validation process
  Example: Convective heat transfer:
  We believe that we have a good understanding of the models, and the code seems to have the models that we want implemented (given our current understanding)
  However, high-quality validation experimental data is missing
  Investment: Experimental campaign for mixed-convective heat transfer

## Slide 9: Review of the Method of Manufactured Solutions (MMS): Providing confidence that the code implementation converges to the proper solution
New, analytically modified system that includes a new source term that we can implement in the code base:
The error is computed to be the difference between the analytical, or manufactured solution and our numerical simulation, Th
We can now refine the mesh and timestep, while computing the error to ensure that the rate of reduction is expected
For example, if we believe our scheme is 2nd or 3rd order in space accuracy, one uniform refinement should reduce the error by 4x or 8x, respectively
We understand that the number of analytical solutions to test our code implementation are very few in number
How can we test the numerical accuracy of our implementation that, in general, solves very complex physics?
Specifically, as we refine the mesh and time step, how does the error respond?
Consider a simple heat conduction PDE:
With given [steady] manufactured solution:

## Slide 10: Review of the Method of Manufactured Solutions (MMS): Providing confidence that the code implementation converges to the proper solution
New, analytically modified system that includes a new source term that we can implement in the code base:
The error is computed to be the difference between the analytical, or manufactured solution and our numerical simulation, Th
We can now refine the mesh and timestep, while computing the error to ensure that the rate of reduction is expected
For example, if we believe our scheme is 2nd or 3rd order in space accuracy, one uniform refinement should reduce the error by 4x or 8x, respectively
We understand that the number of analytical solutions to test our code implementation are very few in number
How can we test the numerical accuracy of our implementation that, in general, solves very complex physics?
Specifically, as we refine the mesh and time step, how does the error respond?
Consider a simple heat conduction PDE:
With given [steady] manufactured solution:

## Slide 11: Spatial Code Verification for a low-Mach, Variable-Density Flow
Density is a function of static enthalpy transport via the standard ideal gas, r = f(P,M,R,T)
Temperature range maps to experiment (see below)
Arbitrary buoyancy source term via rotated gravity vector
Collective study now provides confidence in the interplay between numerical and modeling accuracy
Temperature
Velocity Mag
See, “Exploring model-form uncertainties in large-eddy simulations”, Domino et al, 2016
Kearney experimental configuration

## Slide 12: Solution Verification
Wait, we have a verified code base, however, are running a physics that, while maps to the verification problem, does not have a known solution….
Solution Verification: The process by which we establish that the numerical error associated with a simulation study is quantified
We may be seeking a quantity of interest such, e.g., heat flux to an object, a velocity profile that is of interest, pressure field, drag coefficient, etc.
Ideally, as we refine the mesh, we will see a reduced error
However, an error relative to what? An experiment? Another code result? The other simulations?
Formally, the product of a solution verification study is a convergence rate for a quantity of interest
Richardson Extrapolation: Obtain a series of simulations (that are sufficiently resolved) that are combined to extrapolate to a higher-order solution estimate (given an order of accuracy assumption)
See: Roache, P.J. and Knupp, P.M. (1993), Completed Richardson extrapolation. Commun. Numer. Meth. Engng., 9: 365-374. https://doi.org/10.1002/cnm.1640090502
In practice, most quality studies meet the concept of “solution sensitivity”, i.e., how does the solution vary based on the refined mesh spacing and time step?

## Slide 13: Solution Sensitivity & Due Diligence for Model-form (Structural) Uncertainty
Three meshes (solution sensitivity)
Three models (structural uncertainty)
The heat flux results also show error bars due to time and spatial averaging over a line-of-site
Can we yet feel confidence in any scientific statement? (much closer)

## Slide 14: The Effect of Polynomial (P) and Mesh Spacing (H) Refinement
For the heated cylinder-in-cross flow, either mesh resolution or polynomial promotion provides a more accurate result with more turbulence structure noted
P=1, R0
P=1, R1
P=1, R2
P=2, R0

## Slide 15: Review Case and Conceptual Model: Why are we not converging to the experimental result?
Model Configuration: SNL-based Sean Kearney Experiment, “Experimental investigation of a cylinder in turbulent convection with an imposed shear flow”, AIAA, 2005
Experiment: Outer crossflow, outer cylinder wall, inner hot fluid
QoI: Heat flux… How was that obtained?
  Inverse analysis! Experiment measured temperature and inferred heat flux; an additional error/uncertainty
Iteration on the conceptual model? Add two fluid regions and a CHT coupling to remove the usage of removed the conceptual error an usage of the inverse wall temperature…
Still not perfect, however, we have included many forms of uncertainty in the simulation study
Inflow velocity, wall temperature, etc. are more options

## Slide 16: Review of a Strong V&V Process
Established a sound LES-based V&V process (with uncertainty quantification) that includes the following attributes:
Definition of key physics, PIRT
Code verification
Validation including solution sensitivity
Structural uncertainty, i.e., model form, quantification
Physics assumptions, i.e., your conceptual model
“An assessment of atypical mesh topologies for low-Mach LES”, Domino et al., Comp & Fluids, 2019
Structural UQ
Numerical UQ
Physics UQ
Non-isothermal MMS
10x
reduction

## Slide 17
Tieszen et al. “Validation of a Simple Turbulence Model Suitable
for Closure of Temporally-Filtered Navier-Stokes Equations Using a Helium Plume”, SAND2005-3210

## Slide 18
Tieszen et al. “Validation of a Simple Turbulence Model Suitable
for Closure of Temporally-Filtered Navier-Stokes Equations Using a Helium Plume”, SAND2005-3210
C
M
F
Hidden

## Slide 19
Tieszen et al. “Validation of a Simple Turbulence Model Suitable
for Closure of Temporally-Filtered Navier-Stokes Equations Using a Helium Plume”, SAND2005-3210
C
M
F
xF

## Slide 20
Tieszen et al. “Validation of a Simple Turbulence Model Suitable
for Closure of Temporally-Filtered Navier-Stokes Equations Using a Helium Plume”, SAND2005-3210

## Slide 21: How Code Verification Can Guide Numerical Methods Elucidation

## Slide 22: Consistent vs Lumped Mass Matrix
Goal: Explore the time accuracy of the consistent mass matrix approach on a structured mesh
Convecting Taylor Vortex Case Study: Analytical, transient verification problem
Process: Compute error at a specific time while refining mesh

## Slide 23: Code or Conceptual Error? Part 1: Time Splitting
Case Study: An Algorithm is thought to be second-order-in-time accurate with one nonlinear iteration: True or False?
Issa, “Solution of the implicitly discretized fluid flow equations by operator splitting”, JCP (1985).
  Advent of the “Pressure-implicit with Splitting of Operators”, or PISO
PISO is a scheme that defines a series of predictors and correctors in the context of a fully implicit solve
Conclusion?
Sometimes we code a method correctly, however, have a conceptual error in our understanding of whether or not a scheme is design-order accurate when run in the suggested manner

## Slide 24: Code or Conceptual Error? Part 2: Boundary Conditions
Case Study: Using the convecting Taylor Vortex case, explore boundary conditions
Choice 1: Periodic with specified initial condition
  Requires no formal boundary conditions
Choice 2: Inflow
  Easy, velocity is specified as a Dircihlet
What about pressure? The default approach is to assume a zero normal pressure gradient (no-op) – similar to what would be found at a wall
A notion of a “spurious numerical boundary layer” (Gresho, 1995) shows a characteristic length d ~ sqrt(nDt) error
We also need to make sure that we are adequately converging the nonlinear system within the time step

## Slide 25: Spatial Verification Process
Process:
Start with a mesh of given resolution, Dxo, or a given total node/cell-centered, etc. count, N
Refine the mesh, uniformly, i.e., h-refinement or in polynomial order, p-refinement
Run the series of refinement/promoted meshes and compute an integrated norm over the domain, , for example, below shown to be based on a nodal DOF prediction,
Evaluate error relative to what the precise solution think it should be
  Generally easiest to observe the magnitude of reduction
  For example, , for a first-order in space scheme reduces the error by 2 while for second-order, 4, and third-order, 8, etc.

## Slide 26: Lurking, or Hidden Errors…
In some numerical implementations, an error can exist that is not easily found at a given mesh resolution
For example:
There may be a boundary error that manifests itself locally at a very small subset of the mesh
There may be an error that is a driven by the fidelity of the mesh (consider our specified pressure drop in a pipe example)
Other errors, e.g., for a discrete-ordinance method, we have an underlying quadrature error
skj

## Slide 27: Lurking, or Hidden Errors…
In some numerical implementations, an error can exist that is not easily found at a given mesh resolution
For example:
There may be a boundary error that manifests itself locally at a very small subset of the mesh
There may be an error that is a driven by the fidelity of the mesh (consider our specified pressure drop in a pipe example)
Other errors, e.g., for a discrete-ordinance method, we have an underlying quadrature error
skj

## Slide 28: Lurking, or Hidden Errors…
In some numerical implementations, an error can exist that is not easily found at a given mesh resolution
For example:
There may be a boundary error that manifests itself locally at a very small subset of the mesh
There may be an error that is a driven by the fidelity of the mesh (consider our specified pressure drop in a pipe example)
Other errors, e.g., for a discrete-ordinance method, we have an underlying quadrature error
skj
Quadrature error at given quadrate order

## Slide 29: Temporal Verification: Fixed Spatial Resolution; Reduced Timestep
On a given mesh, compute error at a given time:

## Slide 30: Temporal Verification: Fixed Spatial Resolution; Reduced Timestep
On a given mesh, compute error at a given time:

## Slide 31: Temporal Verification: Fixed Spatial Resolution; Reduced Timestep
On a given mesh, compute error at a given time:

## Slide 32: Temporal Verification: Fixed Spatial Resolution; Reduced Timestep
On a given mesh, compute error at a given time:
At a given mesh, the mesh
spacing is fixed and, eventually,
manifests itself

## Slide 33: Temporal Verification: Reduction of Timestep as Mesh Is Refined
On a series of uniform mesh refinements, compute error at a given time while reducing time step
Must ensure that the spatial error does not dominate:
Traveling Vortex
P1/P1
P1/P2
P2/P2
P2/P1

## Slide 34: Temporal Verification: Reduction of Timestep as Mesh Is Refined
On a series of uniform mesh refinements, compute error at a given time while reducing time step
Must ensure that the spatial error does not dominate:
Traveling Vortex
P1/P1
P1/P2
P2/P2
P2/P1
P2/P1

## Slide 35: Finally…. For Transient Flows, Averaging is Required
The bane of turbulent validation: converged statistics require many flow-through times
Statistical convergence of a given simulation may require many flow-through-times; additional source of uncertainty and/or requirement for quantification of solution convergence

## Slide 36: Essentials of Code Verification: Review
Taxonomy: One verifies code and validates models
Code verification establishes the numerical accuracy of the underlying discretization for the given partial differential equation set
Code verification seeks to provide the temporal and spatial accuracy of the underlying discretization approach
For temporal discretization error,
A two-state Backward Euler time integrator should be first-order in time, specifically the error should scale with Dt
A three-state BDF2 time integrator should scale with Dt2
A multi-stake Runge-Kutta schemes can achieve higher-order accuracy
For spatial discretization error,
A method is design-order if the observed order of accuracy is DxP+1, where P is the underlying basis polynomial order